## Slide 1: Digital ASIC Design Faculty Panel Presentation
Gregory Ling
Will Galles
Jake Hafele
Cade Breeding
Class: CPR E 491
Group: sddec23-06
Client/Advisor: Dr. Duwe
Website: http://sddec23-06.sd.ece.iastate.edu/
[1]
Notes: https://www.pngall.com/microcontroller-png/

## Slide 2: Introduction
Overview
Users
Requirements
Constraints
Market Survey
Gregory Ling

## Slide 3: Overview
ASIC Design
OpenMPW (eFabless)
Open Source
p. 13
[2]
Introduction
[3]
Notes: The ability to create a custom digital ASIC (Application Specific Integrated Circuit) is often locked behind high barriers to entry and restricted to industry professionals. eFabless has provided a free fabrication option named OpenMPW with the requirement that all submissions be open-source, and we will test their manufacturing process and determine its limits. What we learn will be passed down to future users who will use our design as a reference in creating their own for research or other learning tasks.

## Slide 4: Engineering Standards
IEEE 1364-2005 – IEEE Standard Verilog Hardware Description Language
ISO/IEC 9899:2018 – C programming language (C17)
TIA/EIA 232-F – RS232 (UART) Protocol
Serial Peripheral Interface (SPI) Protocol
Wishbone Bus
Inter-Integrated Circuit (I2C) Protocol
p. 15
Introduction

## Slide 5: Users
p. 16
Research
Groups
Our Team
Open Source
Community
Future Teams
Introduction

## Slide 6: Requirements
Explore
Modular design to test different limits of the fabrication process
Learn
Challenge ourselves to work in new areas
Bring-Up Plan
Create a plan for a future group to test our design
p. 13
Introduction
Notes: …

## Slide 7: Constraints
eFabless
10 mm2 user area
SkyWater 130 nm fabrication process
Verilog
Specific folder structure
MPW Precheck
Open-source repository
pp. 13-15
[4]
Introduction

## Slide 8: Market Survey
Production Run
~$1M for full ASIC
Multi-Project Wafer
OpenMPW – eFabless, open-source, funded by Google
ChipIgnite – eFabless, paid ($9,750/project, 10mm2, 4-5 months)
Muse Semiconductor – TSMC, paid ($1,250/mm2, 42 days)
p. 17
Introduction
Notes: Muse lacks tool support

## Slide 9: Design
Functional Modules
Top Level Design
Potential Risks
Resource Cost Estimate
Will Galles

## Slide 10: Module Overview
pp. 49-54
Voice Road-Noise Isolation
Will Galles
Backdoor SPI
Jake Hafele
Clock Gating
Cade Breeding
Standard Cell Test
Cade Breeding
Wishbone Test
Gregory Ling
Custom Cell Test
Gregory Ling
Design

## Slide 11: Backdoor SPI Module
pp. 61-72
Design
Notes: The Backdoor SPI module is a custom external SPI interface to the internal modules that does not require the management microcontroller
It will allow direct communication with modules from outside of the chip to ensure that we are able to externally communicate with the chip.
One of the major design challenges is to clock domain crossing between the external clock domain and our system clock

## Slide 12: Voice Road Noise Isolation Module (DSP)
pp. 50-52
Design
Notes: The Voice Road Noise Isolation module uses a Weiner frequency filter to isolate voice from automotive noise.
This is specifically to test a dense application which will use a large number of gates in the RAM and multiplies.
The purpose of the Voice Road Noise Isolation module is to enhance voice audio from a noisy automotive environment.
The module accomplishes this by implementing a Weiner Filter.
A Weiner Filter is a frequency filter that is carefully crafted to reject frequencies that do not correspond with the human voice.
This module takes in a continuous stream of noisy voice data from an audio source such as a microphone in a car.
It then preforms a convolution with previously generated Weiner Filter.
This convolution applies the filter to noisy audio and the output is a cleaned version of the voice.
This module is primarily there to test how dense we are able to pack the user area.
It will accomplish this because it will require a large amount of multipliers in the convolution unit to be able to process the incoming audio in real time.
We will be able to test how many gates that we can really fit into the user area.

## Slide 13: Top Level Design
pp. 29-31
Design
Notes: This is our modular design with a handful of modules to test different capabilities of the efabless process.
We wanted to test many different aspects of the process all on a single chip, and the modular design builds in a redundancy in case parts of the chip fail to manufacture properly.
For redundancy, we will implement two separate communication busses that are connected to the modules, allowing us to use both the management microcontroller or an external SPI bus to test and control the modules in case one fails

## Slide 14: Potential Risks
pp. 21-22
​Risk ​ | Probability
​No OpenMPW submission is available ​ | ~​40% ​
​DSP module cannot both fit in user area and run at real time ​ | ~​40% ​
​Wishbone bus is unable to interact with user modules after fabrication ​ | ~​5%​
​Fabrication error causes an individual module to fail ​ | ~​15% ​
Design
Notes: We have identified some potential risks that could prevent our project from being a complete success
The first is that there may not be an Open MPW that is taking submissions around the time when we have completed the project.
We will mitigate this by ensuring that our project is completely ready for submission and can turned in either by a future team or by Dr. Duwe
The next risk that we identified was that the Voice Road Noise Isolation Module would not be able to fit in the user area and run in real time
We have tried to mitigate this risk by _______
We then identified a risk with the wishbone bus not being able to interact with the modules inside of the chip.
We mitigated this risk by introducing the backdoor SPI module that would allow us to still communicate with the modules even if their was a failure with the wishbone bus
Lastly we have a risk of individual modules incurring a failure.
We have mitigated this risk by pursuing a modularized approach that will test many different functionalities of the process and the project can still gain valuable data without all of the modules functioning.

## Slide 15: Resource Cost Estimate
Only real cost of the project is our time
eFabless Open MPW Shuttle program funded by Google
All design tools are open source
GitLab and Microsoft Teams provided by the ECpE department
p. 23
Design
Notes: Will
The efbaless open MPW shuttle program is funded by google. Thie means that there is no cost for us to participate in the program. We are able to submit our project without an submission cost. We will eventually get back a handful of our chips back for free after like a year.
There is also no cost associated with the tools as the whole project is meant to be open source. This means that the tools are supported by members of the open source community and are free to us
For now we are using a gitlab instance that was offered to us by the department but one prerequisite for submission is that we host our project in a public repo on github
With every major part of the project having no cost associated with it the only real cost being our time investment into the project

## Slide 16: Testing
Platforms Used
Test Plan
Testing Thus Far
Jake Hafele
Notes: Platforms Used
Test Plan
Testing Thus Far

## Slide 17: Platforms Used
  OpenROAD
    RTL synthesis through GDS Layout
  Magic
  Custom cell layout
  KLayout
  Layout viewer
  GTKWave
  Waveform viewer
p. 23
[4]
Testing
Notes: As gregory mentioned before, there are no financial costs for our project.
Open Source Tools:
OpenROAD
  Used for module hardening and system integration
  Uses RTL design and SkyWater 130 nm Product Development Kit to generate GDSII netlist
  Standard cell process for layout
  Place and route
Magic
  VLSI Layout tool
  Used for custom cell layout
KLayout
  Layout viewer from OpenROAD generation
GTKWave
  View RTL and GL waveform outputs
  Used for unit testing and system integration

## Slide 18: Test Plan
pp. 32-34
Testing
Unit/Regression Testing
RTL Simulations
Gate Level
Simulations
Integration Testing
C Firmware
Simulations
Interface Testing
Bring-Up Plan
Firmware Testing
Document Test Plan
Acceptance Testing
MPW Precheck
Notes: Unit Testing/Regression Testing
  RTL Simulations
    Verilog testbenches
    Instantiate tested modules directly
    Generates waveform output to be viewed with GTKWave
  Gate Level simulation
      Instantiate module through project wrapper
      "Harden" unit under test using OpenROAD
  Regression Testing
      Rerun unit tests if module changed after bugs found in integration
      Can use and update our RTL and GL simulations with original verification
Integration Testing
  Interface Testing
    Wishbone Bus
    Backdoor SPI
    Ensure each module able to send and receive data with BOTH bus protocols
  System Testing
    Test all modules together in combined project wrapper
    Simulate C Code (Very slow)
Acceptance Testing (eFabless Precheck)
  cloned caravel repository includes prechecker by eFabless
  Ensures file structure and modules would pass for fabrication
  Precheck pass needed for MPW submission
Bring-up Plan
  Test Plan
      Write test plan for future design team
      Communication bus interfaces, GPIO, information on MPW return
  Firmware Testing
        Describe firmware needed to interface communication busses
        Describe GPIO needed to test each module

## Slide 19: Testing Thus Far – Adder, Standard Cell
pp. 59-60
Adder Waveform Results
2x1 Standard Cell MUX Waveform Results
Testing
Notes: Use GTKWave as waveform viewer
Adder Waveform
Adder provided by previous May 2023 senior design group 28
Testbench adds two inputs and writes back output into adder
Achieved the goal of running RTL simulation inside toolchain
Standard Cell MUX Waveform
Testing a SkyWater Standard Cell 2-1 MUX directly
3 input combinational circuit, 8 possible outputs
If S = 0, output A0. If S = 1, output A1
Simple test, but tests capabilities of a standard cell if other modules fail

## Slide 20: Testing Thus Far – Backdoor SPI, Shift Out Register
pp. 55-59
Shift Out Register Testbench Verification
Shift Out Register Waveform Results
Testing
Notes: Shift Out Testbench
Tests the shift out register in the Backdoor SPI module
32 bit parallel in serial out shift register, shifting MSB first
Code snippet is verification of serial shift output
  Uses a for loop to check every bit as it is shifted against the input variable shift_in to the task
Can apply error checking for robust unit testing and an accessible bring up plan
Shift Out Waveform
Sample of hex value 0x64 loaded in
32 bit serial shift out begins after i_START is asserted
o_Q is serial output, checked against input of shift out verilog task
If there is a mismatch on a bit, the Q error flag is raised for one clock cycle
If any test fails, the s_Status signal drops to 0

## Slide 21: Future Implementation
Milestones
Schedule
Plan for the Future
Cade Breeding

## Slide 22: Milestones and Schedule
p. 21
Future Implementation
Notes: Here is how we broke down our tasks and planned them out for this semester and the next. Very quick summary of the completed and in progress milestones (go more in depth on the current status in the conclusion).

## Slide 23: Next Steps
RTL Simulation
Integration of Modules
  RTL Simulation
  Gate Level Simulation
Verification
Submission
Bring Up Plan
p. 21
Future Implementation
Notes: Describe each of the steps that are listed. Testing, Submission and Open Source process, Bring up Plan

## Slide 24: Conclusion
Current Status
Contributions
Cade Breeding

## Slide 25: Current Status
p. 43
VRNI (DSP)
Will Galles
Verilog Starting
Backdoor SPI
Jake Hafele
In Testing
Clock Gating
Cade Breeding
Verilog Started
Standard Cell Test
Cade Breeding
Verilog Started
Wishbone Test
Gregory Ling
Verilog Started
Custom Cell Test
Gregory Ling
Exploration
Conclusion

## Slide 26: References
[1] https://www.pngall.com/microcontroller-png/
[2] https://efabless.com/open_shuttle_program
[3] https://www.zerotoasiccourse.com/post/mpw1-bringup/
[4] https://efabless.com/open_shuttle_program
p. 44
Conclusion

## Slide 27: Questions?