## Slide 1: Digital ASIC Design Industry Panel Presentation
Gregory Ling
Will Galles
Jake Hafele
Cade Breeding
Class: CPR E 492
Group: sddec23-06
Client/Advisor: Dr. Duwe
Website: http://sddec23-06.sd.ece.iastate.edu/
[1]
Notes: Web link in chat

## Slide 2: Introduction
Problem Statement
Solution
Requirements
Users
Market Survey
Gregory Ling

## Slide 3: Problem Statement
p. 16
Introduction
The ability to create a custom digital ASIC (Application Specific Integrated Circuit) is often locked behind high barriers to entry and traditionally restricted to teams of industry professionals.
Notes: PAGE NUMBERS,
eFabless has provided a free fabrication option named OpenMPW with the requirement that all submissions be open-source, and we will test their manufacturing process and determine its limits. What we learn will be passed down to future users who will use our design as a reference in creating their own for research or other learning tasks.

## Slide 4: OpenMPW
Multi-Project Wafer
Skywater 130nm PDK
OpenROAD
  Yosys
  Klayout
  Magic
  XSchem
p. 16-18
[2]
Introduction
[3]
Notes: Emphasize lack of institutional knowledge at ISU in transition
eFabless has provided a free fabrication option named OpenMPW with the requirement that all submissions be open-source, and we will test their manufacturing process and determine its limits. What we learn will be passed down to future users who will use our design as a reference in creating their own for research or other learning tasks.
10 mm2 user area
SkyWater 130 nm fabrication process
Verilog
Open-source repository

## Slide 5: Goals
Explore
Modular design to test different limits of the fabrication process
Learn
Expand the knowledge base of open-source fabrication at ISU
Bring-Up Plan
Create a plan for a future group to bring-up our fabricated design
p. 16
Introduction

## Slide 6: Users
p. 19
Research
Groups
Our Team
Open Source
Community
Future Teams
Introduction

## Slide 7: Market Survey and Cost Estimate
Production Run
~$1M for full ASIC
Multi-Project Wafer
OpenMPW – eFabless, open-source, funded by Google
ChipIgnite – eFabless, paid ($9,750/project, 10mm2, 4-5 months)
Muse Semiconductor – TSMC, paid ($1,250/mm2, 42 days)
Our Cost
All design tools are open source
Only real cost of the project is our time
p. 20
Introduction
Notes: Muse lacks tool support

## Slide 8: Design
Design Requirements
Top Level Design
Module Descriptions
Will Galles

## Slide 9: Technical Design Requirements
Create a modular design that would allow for a wide array of operations to take place
Create a redundant system that would still be able to operate if there was a manufacturing failure
Explore new technologies and processes that had not been explored by previous teams
p. 16-18
Design
Notes: Explain that these are very high level point directly to page number assessing them
Open MPW have their own set of submission requirements mention here and explain later

## Slide 10: Wishbone Test Module
p. 85
Design
Purpose
Test on chip communication buses
Notes: The first module in our design is the wishbone test module. It is a module that was created to test the functionality of our primary data in the chip the wishbone bus. As shown here the wishbone bus provides a data bus connection between the test module and the onboard management microcontroller. The module provides this functionality by providing a location where wishbone messages can be reliably written and read from.
The primary purpose for this module is to solidify how to implement and use the wishbone bus.
Wishbone Test
Counter increments every cycle
Read and write via Wishbone bus or backdoor SPI to verify functionality of communication paths
Revealed a bug in the provided management wrapper

## Slide 11: DSP Accelerator Module
pp. 81-83
Design
Purpose
Utilize OpenRAM generated SRAM
Implement a more complex design
Notes: The next module in our design is the Digital Signal Processing accelerator. This module was created to act as a convolutional accelerator for a real time Road Noise Suppression Application. The module is connected to the wishbone bus same as the previous test module. It uses this connection to take in data to store in its integrated memory to be used in the convolution. It also contains a MAC unit that preforms actual convolution and generates the final output. From there the DSP module uses its interrupt connection to the management micro controller to let it know that it has completed the convolution.
In our design analysis we determined that in order to meet the 8kHz sampling rate needed for human voice we would need a clock speed of 8.2 MHz to be able to run in real time.
The main purpose of this module to expand our knowledge of implementing and using the OpenRam generated sram.
Talk about DSP Metrics
DSP
Implements a Convolution accelerator
Data bus connections to wishbone and spi bus to load in data
Interfaces with the two memories that store weights and data values
Mac unit to perform the convolution

## Slide 12: Backdoor SPI Module
pp. 80-81
Design
Purpose
Backup data bus in case of failure
Test crossing clock domains
Notes: The third module in our design is the Backdoor SPI module. This module creates an external SPI connection using the IO ports on the chip. It provides a secondary communication bus in the case that the wishbone bus fails. The module is designed to transfer data across clock domains and synchronize to the internal clock. The internal SPI bus that this module provides has connections to both the wishbone test and DSP modules.
The main purpose of this module was to create a backup data bus within the chip and to test bringing in external data across clock domains.
BackDoor SPI
External SPI interface through IO ports
Extra communication bus if wishbone bus fails
Communicates with wishbone test and DSP accelerator
Handles clock synchronization between SPI Master and Wishbone clocks
  Uses 2 DFF's for control signals as buffer

## Slide 13: Clock Module
p. 83-84
Design
Purpose
Test multiple clock domains
Backup clock in case of failure
Notes: The next module in our design is our Clock module. It is responsible for managing the clock signal running the functional modules in our design. The module implements a clock mux that allows for the internal clock to switch between the management clock provided by the management microcontroller and an external clock brought in by the IO pins. The module also implements clock gating that can be used to turn of individual modules.
The main purpose of this module was to test multiple clocks originating from within and outside the chip along with clock gating individual modules.
Clock Multiplexer
Gating to enable/disable the clock to the user project
Multiplexing to switch between the provided internal clock and an external clock for each clocked module

## Slide 14: Standard Cell & Custom Cell
p. 84
Design
Purpose
Verify base PDK functionality
Perform manual digital layout
Notes: The last two modules in our design are the Standard Cell Test and the Custom Cell test. The standard cell test is just an implementation of a singe cell from the Skywater PDK. It provides a basic test of the PDK’s standard cells’ functionality. The custom cell test is a manually created implementation of a NAND gate. It was created by hand using XSchem and Magic to layout and design the individual metal layers.
The main purpose of these modules are to verify the functionality of the Skywater PDK and to design and implement a custom digital cell.
Standard Cell
Simple AND gate from the standard cell library to provide a baseline test
Custom Cell
NAND gate created manually in XSchem and Magic to try creating a fully custom cell

## Slide 15: Test Overview
Platforms Used
Test Plan
Jake Hafele
Notes: Platforms Used
Test Plan
Testing Thus Far

## Slide 16: Platforms Used
  OpenROAD
    RTL synthesis through GDS Layout
  Magic
  Custom cell layout
  KLayout
  Layout viewer
  GTKWave
  Waveform viewer
p. 25-56
[4]
Test Overview
Notes: As gregory mentioned before, there are no financial costs for our project.
Open Source Tools:
OpenROAD
  Used for module hardening and system integration
  Uses RTL design and SkyWater 130 nm Product Development Kit to generate GDSII netlist
  Standard cell process for layout
  Place and route
Magic
  VLSI Layout tool
  Used for custom cell layout
KLayout
  Layout viewer from OpenROAD generation
GTKWave
  View RTL and GL waveform outputs
  Used for unit testing and system integration

## Slide 17: Test Plan
pp. 36-39
Test Overview
Unit/Regression Testing
RTL Simulations
Gate Level
Simulations
Integration Testing
C Firmware
Simulations
Interface Testing
Bring-Up Plan
Firmware Testing
Document Test Plan
Acceptance Testing
MPW Precheck
SDF Simulations
Notes: Signoff
Meet above 8MHz for DSP to meet real time constraints
SDF Simulations
Can also point out precheck requirements - Unique design/README
XOR check between KLayout and Magic
DRC check

## Slide 18: Implementation
Behavioral RTL
Custom Cells
SRAM
Jake Hafele

## Slide 19: Overview
What is hardening?
  Provides compilation, synthesis, place and route, and signoff all in one package
  Generates hardened macros for submodules AND hardened top-level design
Different implementation techniques
  Behavioral Verilog
  Custom Cell
  SRAM
pp. 40-45
Implementation
[4]
Notes: TODO: incorporate this into one slide describing normal costs and why this being free is good for groups like ourselves?
Will
The efbaless open MPW shuttle program is funded by google. Thie means that there is no cost for us to participate in the program. We are able to submit our project without an submission cost. We will eventually get back a handful of our chips back for free after like a year.
There is also no cost associated with the tools as the whole project is meant to be open source. This means that the tools are supported by members of the open source community and are free to us
For now we are using a gitlab instance that was offered to us by the department but one prerequisite for submission is that we host our project in a public repo on github
With every major part of the project having no cost associated with it the only real cost being our time investment into the project

## Slide 20: Behavioral RTL
Define functionality of modules using Verilog
"Common Case" for most designs
Can be utilized for full design process
Used for:
  Standard Cell Test
  Backdoor SPI
  Wishbone Bus Test
  DSP Accelerator
  Custom Cell (functional verification only)
  Clock MUX (functional verification only)
pp. 40-43
Implementation

## Slide 21: Custom Cell
Create custom cell for use in parallel with SkyWater 130nm PDK
Utilize open-source tools and new process for team and users
Used for:
  Custom Cell (GL verification, hardening)
Unique Process:
  Magic
  XSchem
pp. 40-41
Implementation

## Slide 22: SRAM
Utilizes OpenRAM project for SkyWater 130nm fabrication process
Requirement:
  Had to be placed in top level wrapper
Used for:
  DSP Accelerator (GL verification, hardening)
Unique Process:
  OpenRAM
pp. 42-43
Implementation
Notes: Will
The efbaless open MPW shuttle program is funded by google. Thie means that there is no cost for us to participate in the program. We are able to submit our project without an submission cost. We will eventually get back a handful of our chips back for free after like a year.
There is also no cost associated with the tools as the whole project is meant to be open source. This means that the tools are supported by members of the open source community and are free to us
For now we are using a gitlab instance that was offered to us by the department but one prerequisite for submission is that we host our project in a public repo on github
With every major part of the project having no cost associated with it the only real cost being our time investment into the project

## Slide 23: Project Deliverables
Functional Design
Precheck Pass
Caravel User Guide
Bring-Up Plan
Cade Breeding

## Slide 24: Deliverable 1 – Functional Design
  What was utilized?
  Modular Verilog designs
  Custom NAND cell
  Pre-hardened blackbox designs
  Validated submodule and top-level designs
  RTL Verification
  GL Verification
  C Testing
pp. 88 - 95
Project Deliverables

## Slide 25: Deliverable 1 – Precheck Pass
  Client Request
  Product passes the required precheck for MPW submission
  Perform signoff with SDF simulations
  Delivered Product
  Precheck passes the required tests for submission
  Contents of Product
  Screenshots and code repository proving precheck pass
pp. 43 - 45
Project Deliverables

## Slide 26: Deliverable 2 – Caravel User Guide
pp. 53 - 70
Project Deliverables
  Client Request
  Document implementation processes including behavioral RTL, custom cell, and SRAM
  Document testing process for RTL, GL, SDF, and C testing
  Delivered Product
  Detailed instruction manual with referenced implementation and verification processes
  Contents of Product
  Appendix 8.4.1
Notes: Expand Client Request
Looked at open soure projects and found that many were not properly implementing sram

## Slide 27: Deliverable 3 – Bring-Up Plan
pp. 71 - 75
Project Deliverables
  Client Request
  Plan that future groups can use to verify functionality of manufactured design
  Delivered Product
  Bring up plan that will comprehensively test our design to ensure viability
  Contents of Product
  C tests that can be run on the management soc to verify the device
  Written plan with the startup procedure

## Slide 28: Conclusion
Challenges
Future Work
Final Summary
Cade Breeding

## Slide 29: Potential Risks Identified in Semester 1
pp. 24-25
Conclusion
  No OpenMPW submission is available
  DSP module cannot both fit in user area and run at real time – Success
  Wishbone bus is unable to interact with user modules after fabrication
  Fabrication error causes an individual module to fail
Notes: We have identified some potential risks that could prevent our project from being a complete success
The first is that there may not be an Open MPW that is taking submissions around the time when we have completed the project.
We will mitigate this by ensuring that our project is completely ready for submission and can turned in either by a future team or by Dr. Duwe
The next risk that we identified was that the Voice Road Noise Isolation Module would not be able to fit in the user area and run in real time
We have tried to mitigate this risk by _______
We then identified a risk with the wishbone bus not being able to interact with the modules inside of the chip.
We mitigated this risk by introducing the backdoor SPI module that would allow us to still communicate with the modules even if their was a failure with the wishbone bus
Lastly we have a risk of individual modules incurring a failure.
We have mitigated this risk by pursuing a modularized approach that will test many different functionalities of the process and the project can still gain valuable data without all of the modules functioning.

## Slide 30: Challenges
Conclusion
  LVS problems during hardening
  Updating the PDK version
  Open-source tools come with their own challenges and behave differently then propriety tools.
  Precheck DRC issues with the custom cell
  SDF Simulations are extremely slow

## Slide 31: Future Work
Conclusion
  The next step is to submit to the MPW9 shuttle and receive our fabricated design
  Future testing groups can utilize our Bring-Up Plan deliverable and module specifications to validate our fabricated design.
  Future senior design teams can utilize our Caravel User Guide deliverable to design more complex designs at a faster rate.

## Slide 32: Final Summary
pp. 51
Conclusion
  Design:
  Functional requirements met
  Precheck passed
  Ready for MPW submission and fabrication
  Knowledge:
  Created bring up plan documentation
  Create user guide documentation
  Solved new and existing issues with design processes (Custom cell, SRAM)
Notes: ADD Villiger face and Preche

## Slide 33: References
[1] https://www.pngall.com/microcontroller-png/
[2] https://efabless.com/open_shuttle_program
[3] https://www.zerotoasiccourse.com/post/mpw1-bringup/
[4] https://efabless.com/open_shuttle_program
pp. 52
Conclusion
Notes: TODO: update as necessary

## Slide 34: Questions?

## Slide 35: Supplemental Material

## Slide 36: Constraints
eFabless
10 mm2 user area
SkyWater 130 nm fabrication process
Verilog
Specific folder structure
MPW Precheck
Open-source repository
pp. 16-19
[4]
Supplemental

## Slide 37: Backdoor SPI Module
pp. 100
Supplemental
Notes: The Backdoor SPI module is a custom external SPI interface to the internal modules that does not require the management microcontroller
It will allow direct communication with modules from outside of the chip to ensure that we are able to externally communicate with the chip.
One of the major design challenges is to clock domain crossing between the external clock domain and our system clock

## Slide 38: Voice Road Noise Isolation Accelerator Module (DSP)
pp. 83
Supplemental

## Slide 39
Supplemental
Notes: TODO: verify correctness of diagram

## Slide 40: Does our design look like a Minecraft villager?
Supplemental
https://www.minecraft.net/en-us
Notes: TODO: verify correctness of diagram